## Slide 1: Lecture 31 Music Synthesis
Rob Maher
Electrical & Computer Engineering Montana State University Bozeman, MT USA
rob.maher@montana.edu

## Slide 2: Objective and Subjective
Frequency  Pitch
Sound level  Loudness
Repetition rate  Tempo
Source Geometry  Localization
Spectrum  Timbre

## Slide 3: Timbre
The relative spectral energy at different frequencies is perceived as a distinct tone color, or timbre (pronounced as either tam--burr or tim-burr)
Timbre: The combination of qualities of a sound that distinguishes it from other sounds of the same pitch and volume
Interest in electronically simulating desired timbres

## Slide 4: Some History
Three distinct directions of synthesis development:
Coded Performance (e.g., player piano)
Direct Performance (e.g, keyboard or gestural interface)
Musique Concrete (e.g., tape music)

## Slide 5: ~1900: The Telharmonium
Thaddeus Cahill, inventor
Used a series of geared electrical generators to create harmonics
Before amplifiers: direct power transmission into homes and businesses via telephone wires
Keyboard and potentiometer control
Occupied 30 box cars and weighed 200 tons!

## Slide 7: ~1920: The Theremin
Leon Theremin, inventor
High frequency fixed oscillator (10 MHz)
High frequency variable oscillator adjusted by capacitance (10 MHz)
Capacitance altered by hands moved near antennae:
  Antenna to adjust frequency
  Antenna to adjust volume
Sound is audible “beat” frequency between fixed oscillator and variable oscillator

## Slide 8
https://youtu.be/pSzTPGlNa5U

## Slide 9: ~1928: The Ondes Martenot
Maurice Martenot, inventor
Keyboard instrument with resistance wire
https://youtu.be/f4phKWMaOr0

## Slide 10: ~1928: The Trautonium and Mixturtrautonium
Fredrich Trautwein, inventor
Neon tube oscillator with resistance wire control
Touch-sensitive action
Electric filters for “formants”
https://youtu.be/-tQQEChMq1A

## Slide 11: ~1930: The Hammond Organ
Laurens Hammond, inventor
Frequencies derived from 60Hz power line frequency
Tone wheels with “bumps” pass magnetic pickups
Only 91 sine wave frequencies: all partials are equal-tempered
Frequencies 1 : 2 : 2.9966 : 4 : 5.0397 : etc.
Uses tremolo to eliminate mistuned and “bland” sound
Leslie Loudspeaker – spinning for Doppler vibrato

## Slide 13: Hammond Frequencies
Frequency F (Hz) = M * T * R
  For A4: 20 * 16 * (88 / 64) = 440Hz
  For C#8 = 4,434Hz: 20 * 192 * (74/64) = 4440Hz
91 Hammond tone wheels
  12 tonewheels of 2 teeth
  12 tonewheels of 4 teeth
  12 tonewheels of 8 teeth
  12 tonewheels of 16 teeth
  12 tonewheels of 32 teeth
  12 tonewheels of 64 teeth
  12 tonewheels of 128 teeth
  7 tonewheels of 192 teeth
M – Motor speed, 20 revs/second (1200 rpm)
T – Number of teeth on the tone wheel
R – The gear ratio. This is equal to the number of teeth on the driving gear / number of teeth on driven gear.

## Slide 14
Leslie Loudspeaker
Rotating horns for high frequencies, rotating spinning drum for low frequencies
https://youtu.be/F4XSZ1haPk4

## Slide 15: ~1948: Musique Concrete
Pierre Schaeffer, originator
Use of sound as “found objects”
Everyday sounds used as music
First used phonograph records for sound assembly, then tape recorders

## Slide 16: ~1955: The RCA Synthesizer
Vacuum tube oscillators
Controlled by roll of punched paper tape
Frequency and amplitude controls
Audio output to a disc cutter

## Slide 17: ~1965: Voltage Controlled Synthesizers
Robert Moog
ARP
EMS
Electrocomp
Buchla
Initially monophonic and modular, with patch cords
Later keyboard controlled and portable

## Slide 18
Wendy Carlos

## Slide 19: Voltage Controlled modules
VCO – voltage controlled oscillator
VCA – voltage controlled amplifier
VCF – voltage controlled filter
EG – envelope generator
LFO – low frequency oscillator
Sequencer – memory unit triggered by a clock

## Slide 20
https://www.montana.edu/rmaher/eele217_fl18/soundfiles/Preston_spacerace.wav

## Slide 21: ~1970: Computer Music
Wavetable synthesis (fixed waveform)
Additive synthesis
Modulation techniques (AM, FM, Ring modulation, waveshaping)
Subtractive synthesis

## Slide 22: ~1980-present: Computers as musical instruments
Musical Instrument Digital Interface (MIDI)
Software synthesis
Real time recording direct-to-disk
Real time mixing